## Slide 1: Graft Placement:
Most common cause of technical failure is improper graft placement
Essential for successful ACL reconstruction[8]
Complications caused by poor graft placement cannot be overcome by:
  Best graft strength
  Best fixation strength
  Best rehabilitation program

## Slide 2: Graft Placement:
Principles:
  Impingement:
    Graft impinges on surrounding anatomical boundaries
  Isometry:
    Graft length changes during knee range of motion

## Slide 3: Graft Placement: Isometry
Isometry:
ACL graft length change during knee ROM
  Causes stretching / failure of graft leading to anterior laxity
Oversimplified theory… but still applicable

## Slide 4: Graft Placement: Isometry
Usually determined after ACL graft implanted by measuring graft motion with knee ROM
TOO LATE TO CHANGE !!

## Slide 5: Graft Placement:
SOLUTION:
Computer Assisted ACL reconstruction
    Computer assisted choice of tunnel insertion points based on impingement and isometry
    Computer +/- image guided tunnel placement with increased accuracy and consistency.

## Slide 6: Graft Placement: Computer Guided ACL Recon.

## Slide 7: Graft Placement: Computer Guided ACL Recon.
Painting the Notch:
  Collecting location of impingement anatomy

## Slide 8: Graft Placement: Computer Guided ACL Recon.
Selection of tibial and femoral insertion points:
  Surgeon experience used to select “best” location for ACL

## Slide 9: Graft Placement: Computer Guided ACL Recon.
Non-Image Guided:
  Same principles applied without X-rays

## Slide 10: Graft Placement: Computer Guided ACL Recon.
Collection of Kinematic data:
  Knee moved through ROM
  Impingement & Isometry data collected
  Graft drawn on kinematically determined isometric points with adjustable diameter
  Impingement highlighted on notch “cloud”

## Slide 11: Graft Placement: Computer Guided ACL Recon.
Navigation:
  Computer used to assist in drilling tibial and femoral tunnels in chosen location

## Slide 12: Graft Placement: Computer Guided ACL Recon.
MICCAI Conference 2001, 2003
Navigated Fluoroscopy:
  Find two X-ray cones from source to detector, in local coordinates
  Optical tracking links 3D coordinates of images to the surgical tools, the patient’s anatomy and a library of 3D objects or anatomical models

## Slide 13: Graft Placement: Computer Guided ACL Recon.
CAS OR Setup:
  Collecting location of impingement anatomy

## Slide 14: Graft Placement: Computer Guided ACL Recon.
Painting the Notch:
  Collecting location of impingement anatomy
Selection of ACL insertion points:
  Surgeon experience used to select “best” location for ACL

## Slide 15: Graft Placement: Computer Guided ACL Recon.
Collection of Kinematic data:
  Knee moved through ROM
  Impingement & Isometry data collected
  Graft drawn on kinematically determined isometric points with adjustable diameter
  Impingement highlighted on notch “cloud”

## Slide 16: Graft Placement: Computer Guided ACL Recon.
Non-Image Guided:
  Same principles applied without X-rays

## Slide 17: Graft Placement: Computer Guided ACL Recon.
Tibial Tunnel Planning:
  Computer used to assist in drilling tibial and femoral tunnels in chosen location

## Slide 18: Graft Placement: Computer Guided ACL Recon.
Femoral Tunnel Planning:
  Computer used to assist in drilling tibial and femoral tunnels in chosen location

## Slide 19: Graft Placement: Computer Guided ACL Recon.
Navigation:
  Computer used to assist in drilling tibial and femoral tunnels in chosen location